## Slide 1
NORWEGIAN UNIVERSITY OF LIFE SCIENCES (NMBU)
www.umb.no
Department of Environmental Sciences (IMV), P.D. Jenssen
Wastewater treatment in cold climate -
Source separating systems
Petter D. Jenssen, Faculty of Environmental Sciences and Natural Resource Management (MINA), Norwegian University of Life Sciences (NMBU), petter.jenssen@umb.no,
THT312: Water Management in Cold Regions

## Slide 2: Wastewater treatment options
Constructed
wetlands
Infiltration
Source separation
Conventional systems
Ponds - lagoons

## Slide 3
91
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
www.umb.no
91
(Alsen and Jenssen2005)
Source separation of wastewater
Department of Environmental Sciences (IMV) Petter D. Jenssen

## Slide 4
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
www.umb.no
95
Nutrients and volume of domestic wastewater fractions
(Jönsson et al., 1999).
1 % of the volume contains:
>80% of the resources
Department of Environmental Sciences (IMV) Petter D. Jenssen

## Slide 5: Contribution from the toilet * 90 % of N * 90 % of P * 80 % of K * > 50 % of org. matter * Majority of the pathogens
156
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
www.umb.no
Department of Environmental Sciences (IMV) Petter D. Jenssen
Vinnerås et al. 2006, Todt et al. 2015
Source separation of wastewater
Notes: The majority of the nutrients in wastewater originates from our excreta, urine and feces and ends up in the toilet waste termed blackwater;

## Slide 6: Future toilet types (commercially available today)
157
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
www.umb.no
    Composting /dry sanitation 0 - 0.1 liter/visit
    Urine diverting 0.1 - 4.0 liter/visit
    Water saving (vacuum&gravity) 0.5 - 1.0 liter/visit
Department of Environmental Sciences (IMV) Petter D. Jenssen

## Slide 7
35
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
www.umb.no
A
B
C
Dry/composting toilets
A: single chamber B. Dual chamber C: Removable compartments
Dry or composting toilets can have many different designs and may also use urine diverting toilet bowls. It is possible and preferable to add carbon rich bulking material to improve the C/N ratio. Organic household waste can be used and some designs (A) have a separate chute where organic household waste can be loaded. The bulking material enhances the structure of the compost and covers up fecal matter so as to avoid flies and odour. It can also absorb liquid that is especially important if the urine is not diverted. Many different organic substances may be used as bulking material; ground up bark, sawdust, leaves etc.
Department of Plant and Environmental Sciences, P.D. Jenssen

## Slide 8
Antartica 2001
http://www.polarhistorie.no/hendelser/1209014134.59/tidslinjehendelse_view?geografi=&hovedemne=&underemne=&hovedepoke=&underepoke=&
and
http://www.adlibris.com/no/product.aspx?isbn=8292309020

## Slide 9
Collection
Secondary composting
End product
Troll research station - Antartica
Composting of excreta

## Slide 10
NORWEGIAN UNIVERSITY OF LIFE SCIENCES (NMBU)
Department of Environmental Sciences (IMV), P. D. Jenssen
Conclusions
The compost chamber has a higher temperature than the ambient at all times.
The heat collection is more dependent on sun intensity than the ambient temperature.
Only 10 – 20 % of the solar energy input is utilized by the current design, thus there is room for improvements.
The prototype has potential to sanitize the compost, especially in periods with high sun intensity, and it can substantially increase the efficiency in the cold months.
The system can be modified for dehydration of the excreta.
A solar powered toilet for cold climate

## Slide 11: SUMMER: Solar energy is stored in the ground under or near the building
P. Heyerdahl (2015)
Norges miljø- og biovitenskapelige universitet
Bolig solvarmet hele året

## Slide 12: WINTER: Stored heat is extracted from the ground
Norges miljø- og biovitenskapelige universitet
Bolig solvarmet hele året
P. Heyerdahl (2015)

## Slide 13
NORGES MILJØ OG BIOVITENSKAPLIGE UNIVERITET (NMBU)
www.umb.no
Institutt for miljøvitenskap (IMV) Petter D. Jenssen
Solar panel

## Slide 14
NORGES MILJØ OG BIOVITENSKAPLIGE UNIVERITET (NMBU)
www.umb.no
Institutt for miljøvitenskap (IMV) Petter D. Jenssen
Soldrevet tørr
toalettløsning

## Slide 15
NORGES MILJØ OG BIOVITENSKAPLIGE UNIVERITET (NMBU)
www.umb.no
Institutt for miljøvitenskap (IMV) Petter D. Jenssen
Solar driven toilet - principle

## Slide 16
NORGES MILJØ OG BIOVITENSKAPLIGE UNIVERITET (NMBU)
www.umb.no
Institutt for miljøvitenskap (IMV) Petter D. Jenssen
Dry toilets - how to avoid smell
Extend the ventilation chimney above the highest point of the roof
Use a wind fan
Drain excess liquid
Use bulking material
Use urine diversion

## Slide 17: Dry sanitation - hygiene
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
www.umb.no
4
International research show that dry sanitation may give an equal or higher reduction of pathogens and a high reduction in risk of exposure. (Stenström 2002)
Department of Plant and Environmental Sciences, P.D. Jenssen
(From: Hanssen et al. 2005)

## Slide 18: Future toilet types (commercially available today)
157
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
www.umb.no
    Composting /dry sanitation 0 - 0.1 liter/visit
    Urine diverting 0.1 - 4.0 liter/visit
    Water saving (vacuum&gravity) 0.5 - 1.0 liter/visit
Department of Environmental Sciences (IMV) Petter D. Jenssen

## Slide 19: Urine diverting toilets
41
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
www.umb.no
26
Dual flush: a and b Single flush: c and d
Department of Plant and Environmental Sciences, P.D. Jenssen

## Slide 20: Urine diverting toilets
43
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
www.umb.no
Single flush and dry composting of fecal matter at
Tingvall conference center Sweden
Photo: P.D. Jenssen
Department of Plant and Environmental Sciences, P.D. Jenssen

## Slide 21: Urine diverting toilets
44
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
www.umb.no
Photo: P.D. Jenssen
Single flush and dry composting of fecal matter at
Tingvall conference center Sweden
Department of Plant and Environmental Sciences, P.D. Jenssen

## Slide 22: Urine diverting toilets – dual flush system
46
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
www.umb.no
Urine flushed with 0.1 – 1,6 liters
Faeces - flushed with 2 - 4 liters
(Jønsson et al. 2000)
Department of Plant and Environmental Sciences, P.D. Jenssen

## Slide 23
47
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
www.umb.no
Waterless urinals
Kastrup airport
Copenhagen
Photo: P.D. Jenssen
In waterless urinals urine is collected without the use of water. Provided the urinals are cleaned once per day there is no smell from these urinals.
Department of Plant and Environmental Sciences, P.D. Jenssen

## Slide 24
48
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
www.umb.no
Waterless urinals - Female and male
Photo: Uridan/Jan Moe
48
Department of Plant and Environmental Sciences, P.D. Jenssen
Female
Male (and female)

## Slide 25
NORGES MILJØ OG BIOVITENSKAPLIGE UNIVERITET (NMBU)
www.umb.no
Institutt for miljøvitenskap (IMV) Petter D. Jenssen
Chart: Series 1
| 0 kg | 6 kg | 8 kg | kg N urin | 12 kg N urin | 6 kg N kgj | 8 kg N kgj | 10 kg N kgj | 12 kg N kgj
Series 1 | 91 | 175 | 225 | 265 | 305 | 236 | 318 | 328 | 289
Avling med urin og handelsgjødsel
(Cottis 2000)
0kg 60kg 80kg 100kg 120kg
0kg 60kg 80kg 100kg
Urin
Handelsgjødsel
4000
3000
2000
1000

## Slide 26: Storing of urine General rule: 6 months to achieve hygienization (WHO 2006)
51
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
www.umb.no
Photo: Eco San Res
Both pillow tanks and tanks of harder material as polyester can be used for storing of urine
Department of Plant and Environmental Sciences, P.D. Jenssen
Notes: Urine is collected, by tank trucks, from three housing areas in Stockholm (appr. 350 – 400 inhabitants) transported to storage and reuse at Lake Bornsjön

## Slide 27
Biodiesel from algae grown in urine
(Eikås 2008)

## Slide 28: Future toilet types (commercially available today)
157
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
www.umb.no
    Composting /dry sanitation 0 - 0.1 liter/visit
    Urine diverting 0.1 - 4.0 liter/visit
    Water saving (vacuum&gravity) 0.5 - 1.0 liter/visit
Department of Environmental Sciences (IMV) Petter D. Jenssen

## Slide 29
NORWEGIAN UNIVERSITY OF LIFE SCIENCES (NMBU)
Department of Environmental Sciences (IMV), P. D. Jenssen
23
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
www.umb.no
Low flush toilets
Vacuum
0.5 - 1.5 liters/flush
Gravity
1 liter/flush
Department of Plant and Environmental Sciences, P.D. Jenssen

## Slide 30
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
www.umb.no
Department of Environmental Sciences (IMV) Petter D. Jenssen
Vacuum toilets - energy use
4 Kwh/person and year

## Slide 31
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
www.umb.no
Department of Environmental Sciences (IMV) Petter D. Jenssen
Vacuum toilets - dual flush
Average water use/flush about 0.5 liters
Dual flush
Low noise

## Slide 32: Kildesep prinsipp
25
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
www.umb.no
Toilet waste (blackwater) +
organic household waste (OHW)
Vacuum or low flush gravity toilets
Source separating system - logistics
OHW
BW
Using vacuum toilets any building can be served. Organic household waste (OHW) can be integrated in the system using kitchen grinders or a common grinder at the discharge to the collection tank.

## Slide 33: Kildesep prinsipp
25
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
www.umb.no
Toilet waste (blackwater) +
organic household waste (OHW)
Vacuum or low flush gravity toilets
Source separating system - logistics
OHW
BW
Greywater

## Slide 34: Kildesep prinsipp
25
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
www.umb.no
Toilet waste (blackwater) +
organic household waste (OHW)
Vacuum or low flush gravity toilets
Source separating system - logistics
OHW
BW
Greywater
Biogas CH4

## Slide 35: Kildesep prinsipp
Thermophilic anaerobic
treatment - BIOGAS
Growth medium
Nutrients
Heat
CO2
CHP - combined heat
and power
El.
OHW
BW
January 11, 11
Source separating system - circular economy
SiEUGreen Horizon 2020

## Slide 36: Kildesep prinsipp
Thermophilic anaerobic
treatment - BIOGAS
Growth medium
Nutrients
Heat
CO2
CHP - combined heat
and power
El.
OHW
BW
Source separating system - circular economy
Local nutrient recycling
January 11, 11
SiEUGreen Horizon 2020

## Slide 37: Kildesep prinsipp
Thermophilic anaerobic
treatment - BIOGAS
Growth medium
Nutrients
Heat
CO2
CHP - combined heat
and power
El.
OHW
BW
Source separating system - circular economy
Local nutrient recycling
January 11, 11
SiEUGreen Horizon 2020

## Slide 38
91
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
www.umb.no
91
(Alsen and Jenssen2005)
Source separation of wastewater
Department of Environmental Sciences (IMV) Petter D. Jenssen
Greywater
treatment

## Slide 39: Wastewater treatment options
Constructed
wetlands
Infiltration
Source separation
Conventional systems
Ponds - lagoons

## Slide 40
NORGES MILJØ OG BIOVITENSKAPLIGE UNIVERITET (NMBU)
www.umb.no
Institutt for miljøvitenskap (IMV)
BOF < 5 mg/l
SS < 2 mg/l
E.coli 2-3 log reduction
Compact greywater treatment system
Heistad (2015)

## Slide 41
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
www.umb.no
Department of Environmental Sciences (IMV) Petter D. Jenssen
Potential for making very compact greywater treatment systems
Membrane bioreactor systems (MBR´s)

## Slide 42
91
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
www.umb.no
91
(Alsen and Jenssen2005)
Source separation of wastewater
Department of Environmental Sciences (IMV) Petter D. Jenssen
Treatment - BOD, TSS, nutrients | HIGH
Treatment - Hygiene | HIGH
Treatment - Organic micropollutants | HIGH
Investment cost | MEDIUM/LOW
O & M | LOW/MEDIUM
Technical complexity | LOW/HIGH
Suitability arctic conditions | HIGH

## Slide 43: Conclusions
Source separating solutions are designed for reclamation and recycling of wastewater resources - circular economy
Source separating solutions can be used for single households apartment buildings or upscaled to do towns or cities
Source separation has potential for very low water use and production of bioenergy fertilizer and soil amendment products
Dry toilets are not inferior to flush toilets if constructed right and have a large potential for optimization and adaption to cold climate
Dry sanitation may give an equal or higher reduction of pathogens and a high reduction in risk of exposure
A new generation vacuum toilets cuts average flush volume to about 0.5 liter
Source separation opens for very compact – inhouse – greywater treatment systems
Source separation facilitates removal of organic micropollutants´s as PPCP´s
NORGES MILJØ OG BIOVITENSKAPLIGE UNIVERITET (NMBU)
www.umb.no
Institutt for miljøvitenskap (IMV) Petter D. Jenssen

## Slide 44
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
www.umb.no
Department of Environmental Sciences (IMV) Petter D. Jenssen
Alsen, K. and P.D. Jenssen. 2005 Ecological sanitation – an option for all. Norwegian University of Life Sciences. 39 p.
Gunnarsdóttira, R., K. Müller, P. E. Jensen, P.D., Jenssen, and A. Villumsen, (2012). Effect of Long-Term Freezing and Freeze−Thaw Cycles on Indigenous and Inoculated Microorganisms in Dewatered Blackwater. Environ. Sci. Technol., 46: 12408−12416
Gunnarsdóttira, R., Jenssen, P.D., Jensen, P.E., Villumsen, A., Kallenborn, R., (2013). A review of wastewater handling in the Arctic with special reference to Pharmaceuticals and Personal Care Products (PPCPs) and microbial pollution, 2012. Ecological Engineering, 50, pp.76– 85.
Hennessy, T.W., Ritter, T., Holman, R.C., Brüden, D.L., Yorita, K.L., Bulkow, L.,
Cheek, J.E., Singleton, R.J., Smith, J., 2008. The Relationship between In-Home Water Service and the Risk of Respiratory Tract, Skin, and Gastrointestinal Tract Infections Among Rural Alaska Natives. American Journal of Public Health. 98 (11) 2072-2078.
Jenssen P.D, P.H. Heyerdahl, J.F. Hanssen and M.E. Kelova, 2015. Solar powered dry toilet for cold climate. Results from a pilot study. Poster presentation at the 5th International Dry Toilet Conference. Tampere, Finland 19-22/8-2015.
Johnsen, K. 2016. A brief history of the past 60 years of water and sanitation practices in the arctic. Presentation at the conference: Sanitation in cold climates. Sisimiut Greenland, 12-18. April. Arctic Technology Centre, DTH, Copenhagen.
Kallenborn, R., Fick, J., Lindberg, R., Moe, M., Nielsen, K.M., Tysklind, M., Vasskog, T., 2008. Pharmaceutical residues in Northern European environments: consequences and perspectives. In: Kümmerer, K. (Ed.), Pharmaceuticals in the Environment. , 3rd ed. Springer Verlag, New York, Tokyo, Heidelberg, 522 p.
Rogers, J., C. Schulz, C. Nelson. 2016. The Alaska Water Challenge. Presentation at the conference: Sanitation in cold climates. Sisimiut Greenland, 12-18. April. Arctic Technology Centre, DTH, Copenhagen.
Todt D. and P.D.Jenssen ,2015. Particle removal in a novel sequential mechanical filter system loaded with blackwater. Water Science and Technology, 71 (9): 1407-1413.
U.S. Congress, 1994. U.S. Congress, Office of Technology Assessment, An Alaskan Challenge: Native Village Sanitation, OTA-ENV–591.Washington, DC: U.S.Government Printing Office, May 1994.
References

## Slide 45
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
www.umb.no
Department of Environmental Sciences (IMV) Petter D. Jenssen
References continued
Gallagher, N.T., Sharvelle, S.E., 2010. Decentralized Anaerobic Blackwater Management: A Sustainable Development Technology Concept for Urban Water Management. World Environmental and Water Resources Congress 2010: Challenges of Change. Proceedings of the World Environmental and Water Resources Congress 2010.
Jenssen, P.D., Greatorex, J., Warner, W.S., 2004. Sustainable wastewater management in urban areas. In K. Kayser (ed.) "Konzeptionen Dezentralisierter Abwasserreinigung und Stoffstrommanagement" (concepts of de-centralized wastewater treatment and resource management). Universitat Hannover Weiterbildendes Studium Bauingenieurwesen "Wasser und Umwelt", 51p.
Smith, D.W., Low, N., 1996. Cold regions utilities monograph, third ed. Technical Council on Cold Regions Engineering, American Society of Civil Engineers and Cold Regions Engineering Division, Canadian Society for Civil Engineering.
Umhverfisstofun (UST), 2003. Staða mála hvað varðar hreinsun skólps á Íslandi, skýrsla Umhverfisstofunanar sbr. 28. gr. reglugerðar nr. 798/1999, um fráveitur og skólp (report in Icelandic. English title: Status of wastewater treatment in Icland)
Vogelsang, C., Grung, M., Jantsch, T.G., Tollefsen, K.E., Liltved, H., 2006. Occurrence and removal of selected organic micropollutants at mechanical, chemical and advanced wastewater treatment plants in Norway. Water Research 40, 3559-3570.
Winker, M., Faika, D., Gulyas, H. and Otterpohl, R. (2008). A comparison of human pharmaceutical concentrations in raw municipal wastewater and yellowwater. Science of the Total Environment. 399 (1-3), 96-104.

## Slide 46
Thank you!
petter.jenssen@nmbu.no