## Slide 1: Waste water in the north – concerns and treatment
Pernille Erland Jensen
Associate Professor
Head of studies BEng Arctic Technology
Department of Civil Engineering
Technical University of Denmark (DTU)

## Slide 2: Overall content
Wastewater characteristics and concerns
Current wastewater management in he north
Experimental wastewater management in Greenland

## Slide 3: Arctic Engineering at DTU
DTU Campusses

## Slide 4: Waste water – characteristics and concerns
Pernille Erland Jensen
Associate Professor
Head of studies BEng Arctic Technology
Department of Civil Engineering
Technical University of Denmark (DTU)

## Slide 5: Lecture content
What is wastewater
How do we characterize wastewater
How does was wastewater in the north compare to that from elsewhere?
Which environmental effects are observed?

## Slide 6: What is waste water?
Toilet waste
Kitchen drain
Bath drain
Laundry
Rain water
Industrial wastewaters
Domestic waste water
Grey water
Black water
Combined sewers

## Slide 7: What does wastewater contain?
Color, Odor
Nutrients
Organic matter
Heavy metals
Other Salts
Grease
Microoroganisms
Particles

## Slide 8: How do we commonly characterize wastewater
Solids
TSS (Total Suspended Solids) + other definitions of solids TDS, SS, Fixed, Volatile.
Organic matter
BOD5 (Biological oxygen demand, 5 days, 20°C or TOC, COD, VOC
Nutrients
Nitrogen incl. various speciations: organic, free, nitrite, nitrate, ammonia
Phosphorous Organic, Inorganic
Salts
Cl
SO4
Grease
Microoroganisms
Total coliform

## Slide 9: But there is more to the story
Chemicals
Heavy metals
Personal care products
Medical residues
Micro plastics
Nano-materials
…

## Slide 10: And the microbiology is more than just coliforms
E. coli – and gram negatives
Enterococci - and gram positives
Viruses
Helmints

## Slide 11: How does wastewater in the north compare to wastewater other places?
 | Typical composition1 |  |  | Sisimiut |  |  | Kanger-lussuaq | DK limit5
 | Weak | Medium | Strong | 20113 | 20134 | 20132 |  | 
COD (mg/L) | 250 | 500 | 1000 | NA | 143 | 400-700 | 6369 | 75
N (mg/L) | 20 | 40 | 85 | 46-130 | 30 | NA | 5-518 10-609 | 8
P (mg/L) | 4 | 8 | 15 | 4-8 | 3 | 10-15 | 5-138 0.4-109 | 1.5
Total coliforms | 106 -107 | 107-108 | 108-109 | 105 -106 | 106 -107 | NA | 107-10810 | NA
Entero-cocci |  | 102-103 |  | 104 -105 | 104 -106 | NA | 105-10610 | NA
Red number refer to reference (last slide)
Notes: Red numbers refer to background literature

## Slide 12: References
Tchobanoglus, G. & Burton, F. Wastewater Engineering, Treatment, Disposal and Reuse, Third Edition, Metcalf and Eddy, Inc., McGraw –Hill, Inc. 1991.
Drastrup, E.M., Petersen, S. B., Evaluering af effekten af et mekanisk-kemisk rensningsanlæg i Sisimiut, BSc Thesis (in Danish), ARTEK, DTU, 2013.
Martinsen, G., Nicolaisen, E.S. , Karakterisering af spildevand i Sisimiut, Grønland, med særligt fokus på antibiotikaresistente bakterier, BSc Thesis (in Danish), ARTEK, DTU, 2011.
Davidsen, S., Toke, J. Metoder til rensning og desinfektion af kloakeret spildevand I arktiske områder med få indbyggere, BSc Thesis (in Danish), ARTEK, DTU, 2013.
Miljøministeriet (2016) BEK nr 153 af 25/02/2016.
Selvstyrets bekendtgørelse nr. 10 af 12. juni 2015 om bortskaffelse af latrin og spildevand http://lovgivning.gl/lov?rid={0D5348FF-3943-4739-B3E9-9897D8B93713}
COWI Consultants 2006. Udrednings- og pilotprojekt vedr. håndtering af gråt spildevand i de grønlandske byer og bygder, Miljøstyrelsen (Danish EPA).
Mathiasen, L.V., Rosing Hansen, C.M., Freiberg, T. Analyser af Spildevand i Kangerlussuaq, Student report (In Danish), ARTEK, DTU, 2015.
Konring, A., Tang, C. Wastewater treatment potentials in Kangerlussuaq: Characterisation of flow and chemical loadings, Student report (In Danish), ARTEK, DTU, 2015.
Chhetri, R.; Klupsh, E., Andersen, H.R., Jensen, P., Treatment of Arctic wastewater by chemical coagulation, UV and peracetic acid disinfection, Environ Sci. Pollut. Res., DOI 10.1007/s11356-017-8585-5.
All student works may be found here: http://find.artek.byg.dtu.dk/pubs/frontpage/

## Slide 13: Observed environmental effects: Visibility

## Slide 14: Observed environmental effects (no treatment)
Floating items on surface
Eutrophication
Heating
Dead bottom of bay
Ecosystem disturbance*
Heavy metal accumulation in sediments**
Antibiotic resistance***
Health effects?
New wastewater regulation implemented in 20156
Leading out grey water to terrain may be problematic7
References
*Bach, L. and Dahllöff, I. 2012, Local contamination in relation to population genetic diversity and resilience of an arctic marine amphipod. Aquatic Toxicology, 114-115, 58-66.*Bach, L., Fischer, A. and Strand, J. 2010, Local anthropogenic contamination affects the fecundity and reproductive success of an Arctic amphipod. Marine Ecology Progress Series, 419, 121-128.
**Villumsem,A. and Ottosen,L. 2006, Heavy metal and TBT contamination in the sediment around Sisimiut, Greenland, Proceedings of ARTEK Event 2006, pp. 21-23.
***Maria Granberg
Eutrophication

## Slide 15: Elevated concentrations of heavy metals and anthropogenic compounds
Pedersen, K. B., Lejon, T., Jensen, P. E., & Ottosen, L. M. (2015). Chemometric Analysis for Pollution Source
Assessment of Harbour Sediments in Arctic Locations. Water, Air, and Soil Pollution, 226(5), 1-15. DOI:
10.1007/s11270-015-2416-4
H4: Sewage outlet, all others harbor activity, H: Hammerfest, S: Sisimiut

## Slide 16: Ecosystem disturbance
Bach, L. and Dahllöff, I. 2012, Local contamination in relation to population genetic diversity and resilience of an arctic marine amphipod. Aquatic Toxicology, 114-115, 58-66.

## Slide 17: Ecosystem disturbance
Bach, L., Fischer, A. and Strand, J. 2010, Local anthropogenic contamination affects the fecundity and reproductive success of an Arctic amphipod. Marine Ecology Progress Series, 419, 121-128.

## Slide 18: Antibiotic resistance
http://www.artek.byg.dtu.dk/english/-/media/Centre/Artek/artek_english/artek%20events/ARTEK-Event-2016/Presentations_web/Session_1/Maria-Granberg.ashx?la=da
There is a difference in resistance patterns between unexposed and exposed areas
Ciprofloxacin, Tetracyclin and Macrolide resistance is only found near the sewage outlet.
β-lactam resistance is found everywhere as is one type of aminoglycoside resistance. This may be attributed to an extended heavy use of β-lactam antibiotics or natural occurrence of β-lactam and aminoglycoside resistance in nature.
Sediment bacterial communities from exposed sites differ from and are less diverse than communities from unexposed sites
Sediment bacterial community function at the sewage outlet shows signs of eutrophication impact
Bacterial abundance is severely reduced in guts of marine organisms living in the vicinity of the sewage outlet
Resistance patterns are replicated at different trophic levels along the exposure gradient
This indicates food chain transfer of ARG or resistant bacteria, and may be a potential risk for humans.

## Slide 19: Waste water management in the North
Pernille Erland Jensen
Associate Professor
Head of studies BEng Arctic Technology
Department of Civil Engineering
Technical University of Denmark (DTU)

## Slide 20: Lecture content
Conventional treatment recap
Challenges in the north
How is wastewater handled currently in the north?
Effects of treatments
  Examples from Iceland, Faroe Islands, Norway, Canada and Greenland

## Slide 21: Conventional treatment recap
Treatment level | Method | Effect
Preliminary | Screening | Large particles removal
Primary | Screening and/ or sedimentation | Smaller particles removal, sand, fraction of OM inkl. some P, fraction of HM’s and other compounds bound to OM.
Secondary | Chemical and/or biological treatment (e.g. flocculation/ biological conversion and sedimentation) | Smaller biodegradable organics and suspended solids. Disinfection effect.
Tertiary | Biological treatment and or chemical (e.g. precipitation of nutrients with Fe and Al salts, fluctuating oxygen /anaerobic) | High level nutrient removal. Disinfection effect.
Advanced | Various additions | Depending on need

## Slide 22: Effects of climate
Water viscosity increases
  Mixing reduced
  Sedimentation slows down
  Filtration slows down
Longer survival of pathogenic bacteria
Metabolic (biological) and chemical reaction rates slow down:
  Often by 2-3 times per 10 °C temperature reduction (Arrhenius equation)
Increased retention time
High energy costs
High investment cost
Unreliable energy supply
Permafrost and other unstable site conditions OR surface bedrock
Small communities
Remoteness challenging during constructional and operational resupply
Lack of specialists on site
High investment cost per person
High maintenance cost
High risk of failure
Effects of geography

## Slide 23: Present management of waste water the North
Wastewater lagoons (photo: Lisbeth Truelstrup Hansen)
Mechanical plants – primary/secondary (photo: Kenneth Johnson)
No treatment
Secondary treatment for towns > 20.000persons
Smaller places no treatment
Primary treatment
No treatment

## Slide 24: Wastewater in Greenland
Sewers in most of towns.
Bag toilets or septic tanks for the rest, grey water directly into environment.
All wastewater let out untreated at shoreline.

## Slide 25: Wastewater in Greenland
In settlements modern replacement for honey buckets is needed:
  Convenience
  Dignity
  Environment

## Slide 26: Wastewater in Greenland
In 2005 report concluded that no harm to the environment was to be expected from current practise *
BUT report also clearly states:
Only nutrients are considered, not e.g. pathogens, heavy metals or anthropogenic compounds.
The evaluation anticipates that the outlet is in open water and not closed Fjords.
New legislation requires municipalities to make environmental impact assessment of recipients and implement treatment of wastewater if impacts are observed **
Water quality criteria set for wastewater from mineral extraction projects***
*COWI Consultants 2005. Udrednings- og pilotprojekt vedrørende håndtering af miljøproblemer som følge af spildevand i de grønlandske byer. Miljøstyrelsen (Danish EPA).
**Selvstyrets bekendtgørelse nr. 10 af 12. juni 2015 om bortskaffelse af latrin og spildevand: http://naalakkersuisut.gl/~/media/Nanoq/Files/Kundgoerelser/DK/2015/Bekendtgoerelser/bkg_10%20dk.pdf
***http://naalakkersuisut.gl/~/media/Nanoq/Files/Hearings/2015/Nye%20retningslinjer%20for%20udarbejdelse%20af%20VVM%20for%20mineprojekter%20i%20Groenland/Documents/EIA%20Guidelines_UK_.pdf

## Slide 27: Faecal bacteria on seaweeds in Greenland
Faecal bacteria on seaweeds in Greenland
Kreissig, Katharina Johanna ; Hansen, Lisbeth Truelstrup ; Jensen, Pernille Erland , 2017, Poster presented at: 7th Nordic seaweed conference, 2017, Grenaa. http://orbit.dtu.dk/ws/files/140631837/Nordic_Seaweed_Conference_KJKR_poster_final.pdf

## Slide 28: Micropollutants in wastewater in four arctic cities - is the treatment sufficient?
Treatment types
LSH (Hospital, Torshavn): Primary and secondary treamtent (mechanical biological)
Serjsjantviking (Torshavn): Primary treamtent (settling and flotation), uncontrolled secondary treatment may happen in the tank (septic tank type reactions)
Breivika (Tromsø): Primary treatment (filtering)
Langenes (Tromsø) : Primary treatment (filtering)
Klettag (Reykjavik): Primary Treatment (mechanical settling)
Ánanaust (Reykjavik): Primary Treatment (mechanical settling)
Sisimiut (Greenland): None
Micropollutants in wastewater in four arctic cities - is the treatment sufficient?
Maria Dam, Guðjón A. Auðunsson, Hans H. Poulsen, Ingrid A. Berg, Lone Kristensen, Jan Stenersen, Fríðbjørg N. Joensen, Vivie K. Davidsen, and Susanne B. Petersen
ISBN 978-92-893-5121-8 (PRINT), ISBN 978-92-893-5123-2 (PDF), ISBN 978-92-893-5122-5 (EPUB), http://dx.doi.org/10.6027/TN2017-550, TemaNord 2017:550, ISSN 0908-6692, Standard: PDF/UA-1, ISO 14289-1
© Nordic Council of Ministers 2017

## Slide 29: Effect of primary wastewater treatment
Treatment types
LSH: Primary and secondary treamtent
Serjsjant: Primary, occationally secondary
Sisimiut: None
All others: Primary

## Slide 30: Common Nordic Project results
Treatment types
LSH: Primary and secondary treamtent
Serjsjant: Primary, occationally secondary
Sisimiut: None
All others: Primary

## Slide 31: LAS (linear alkylbenzene sulphonates (LAS), anionic surfactants in detergents )
Treatment types
LSH: Primary and secondary treamtent
Serjsjant: Primary, occationally secondary
Sisimiut: None
All others: Primary

## Slide 32: Cadmium
Treatment types
LSH: Primary and secondary treamtent
Serjsjant: Primary, occationally secondary
Sisimiut: None
All others: Primary

## Slide 33: Phtalates
Treatment types
LSH: Primary and secondary treamtent
Serjsjant: Primary, occationally secondary
Sisimiut: None
All others: Primary

## Slide 34: PFAS
Treatment types
LSH: Primary and secondary treamtent
Serjsjant: Primary, occationally secondary
Sisimiut: None
All others: Primary

## Slide 35: Overall conclusions on effect of treatments
TOC: Reduced
Nutrients (P,N): Some effect
LAS: Some effect
PAH: No effect
Phenols: No reduction effect
Mercury: No effect – except Klettagardar
Phthalates: Reduced
PFAS: No effect – except Langnes

## Slide 36: Canada – experience with lagoons
New legislation in Canada – January 2015
Northwest Territories, Nunavut, and northern regions of Quebec and Newfoundland and Labrador are temporarily exempt.
http://www.ec.gc.ca/eu-ww/

## Slide 37: Experimenting wastewater handling in Greenland
Pernille Erland Jensen
Associate Professor
Head of studies BEng Arctic Technology
Department of Civil Engineering
Technical University of Denmark (DTU)

## Slide 38: Chemical mechanical treatment in container size

## Slide 39: Results pilot scale experiments
COD in untreated and treated wastewater
BOD5 in untreated and treated wastewater

## Slide 40: Results pilot scale experiments
Phosphorous in untreated and treated wastewater

## Slide 41: Heavy metals

## Slide 42: How about hygiene
Lab scale (jar test) + PAA disinfection

## Slide 43: Results, coliforms and enterococci* removal
*Max 35 CFU/100mL in recreational waters US
Chhetri, R.K., Klupsch, E., Andersen, H.R., Jensen, P.E., Treatment of Arctic Wastewater by Chemical Coagulation, UV and Peracetic Acid Disinfection, Environmental Science and Pollution Research, DOI: http://dx.doi.org/10.1007/s11356-017-8585-5, 2017.

## Slide 44: Test of composting toilets
Feasibility of installing composting toilets in selected houses, Sarfannguit, Greenland.
Green: feasible
Yellow: can become feasible Blue: too small
Red: non feasible
Bak, A.M.; Mogensen,C.S.J.; Munck, M.H. (2017), Sanitære forhold i Sarfannguit, report, course 11837 AT sommerprojekt, DTU.

## Slide 45: Challenges honey bag toilets
Citizens would indeed like more convenient and decent solutions.
Would prefer water flushed toilets, nut are open towards composting toilet solutions.
Composting toilets should theoretically be able to work fine in Greenland since they do in other northern places.
Observed challenges:
Houses too small
Rooms too cold (in Winter time)
Tested toilets designed for 4 persons, but many families are larger
Energy expenditure – when you live from fishing and hunting
Imported stabilization material – also a cost
Instructions in swedish
No running water in the room

## Slide 47
Gunnarsdóttir, R.; Heiske, S.; Jensen, P.E.; Schmidt, J.E.; Villumsen, A; Jenssen, P.D. Effect of anaerobiosis on indigenous microorganisms in blackwater with fish offal as co-substrate, Water Research, 63, 1-9, 2014.

## Slide 49
Gunnarsdóttir, R.; Müller, K;. Jensen, P. E.; Jenssen, P.; Villumsen, A. Effect of long-term freezing and freeze/thaw-cycles on indigenous and inoculated microorganisms in dewatered blackwater, Environmental Science & Technology, 46, 12408-12416, 2012

## Slide 50: Combined composting and freeze-thaw dewatering in Iqaluit, Nunavut
Freeze thaw cycles:
Causes particles to coagulate
Improves dewater ability significantly
Johnson, K., Sewage Composting in Iqaluit, Nunavut – Black Gold, in: Water (the new gold), proceedings of WCW Conference & Trade Show, Winnipeg, September 20 – 23, 2009.

## Slide 51: Post treatment conditioning
Untreated sludge may not be used as fertilizer
Stabilized sludge can be used with restrictions (not for food production, private or public parks). Must be dug into the soil within 6 hours.
After controlled composting can be used with restrictions (not for food production, private or public parks).
Unrestricted use after hygienization:
Heat treatment
Pasteurisation
Drying
Thermal reduction

## Slide 52
Aka Høegh, mother of the sea